## Slide 1
Bangladesh University of Engineering and Technology
Department of Electrical and Electronic Engineering
Project Presentation eee 304_B1
Date: 03/12/2024
FPGA-Powered Real-Time Quizzing System
Prepared by:
Sheikh Tariful Islam(2006066)
Md Al Saif Hossain Anay(2006077)
Md Nakib(2006091)
Md. Mostafizur Rahman(2006096)
Submitted to:
Nafis Sadik
Lecturer
Department of EEE,BUET
H M Tahmeed-Ul-Islam
Lecturer(PT)
Department of EEE,BUET

## Slide 2
Overview
Introduction
Objective
Workflow
Methodology
Hardware Implementation
Work Progress
Individual Contribution
Demonstration
Different Segment of Main Code

## Slide 3: Introduction
FPGA (Field Programmable Gate Array) board is a great way to implement high performing automated system like quizzing system.
FPGA board is a good choice where real time processing, low latency and scalability is required

## Slide 4: Objective
Design a user friendly quizzing system
Implement complete quizzing system – including question selection, answer processing, score calculation and winner declaration
Showcase FPGA capabilities – demonstrating flexibility and performance advantages of FPGA

## Slide 5: Work Flow
Team D
Judge
Yes/No
Store the score
Team A
Team B
Team C
Team Selection
Ans within 10sec
Adds point to Score
Doesn't add any point to score
Initial Score
5
6
3
4
Team B
Lets Assume Team B has pressed the Buzzer First
Yes
Given Answer by Team B is correct hence Judge presses yes
Team B will get 1 point
So the total point will be 7
This new score will be stored for further comparison
NO
Yes

## Slide 6: Work Flow
Score of Team A
Score of Team B
Score of Team C
Score of Team
Comparator
Winner Declaration
Final Score
5
7
3
4
Comparator will pass Team B
Team B will be declared winner
Master Reset
Push the Button
The whole game will be reset

## Slide 7: Methodology
Team Selection
Time Counter
Answer Evaluation
Score Update
Winner Declaration
System Reset

## Slide 8: Methodology
TeamB
Team Selection
TeamA
TeamB
TeamC
TeamD
Whoever Presses the buzzer first will get the chance to answer

## Slide 9
Verilog Code:
Vector Wave Form:
Team Selection

## Slide 10
Once a Team is selected the timer will start counting time
In our quizzing system we will give 10 sec to answer a question
If the question is not answered within the time no points will be added
Verilog code for timer
Time Counter

## Slide 11
Time Counter
Vector Wave Form

## Slide 12: Answer Evaluation
If the answer is right, judge will press yes button
If the answer is wrong then judge will not press any button

## Slide 13: Score Update
If judge press yes button then score of the team that has pressed the buzzer first will increase
Other wise the score will be the same as previous
Verilog code

## Slide 14: Score Update
Vector Wave Form

## Slide 15: Winner Declaration
The team that has scored highest will be the winner
Winner team's score will be displayed in FPGA using the 7 segment display
Team num of the winning team will be showed using a ouput LED
Verilog Code:

## Slide 16: Winner Declaration
Vector Wave Form

## Slide 17: System Reset
Reset:
After every question answer the buzzer needs to be prepared for next question
Using Reset button we complete this work
Master Reset:
Once a match is completed whole system needs to be reset
Master Reset serves this purpose

## Slide 18: Hardware Implementation
Description of Input Switches:
Team A
Team B
Team C
Team D
Winner
Declaration
Correct
Reset
Master Reset

## Slide 19: Hardware Implementation
Description of Output LEDs:
Team A
Team B
Team C
Team D
Time Up
(10 sec)
Buzzer Locked

## Slide 20: Hardware Implementation
Description of 7 Segment display(Used as an output):
7segment display is used for showing the time counting
It will also show the number of the participant who answered the question

## Slide 21: Hardware Implementation
Description of DOT Matrix Display(used as an output):
In the DOT Matrix the selected team(who presses the buzzer first) is displayed

## Slide 22
Count down has started
Team 4 presses the buzzer first
The buzzer is locked
Hardware Implementation
Team Selection:

## Slide 23
Time is up
Time up indicating light is on
Given Answer is correct
Total point of Team 4 is increased
Hardware Implementation
Evaluation:

## Slide 24
Hardware Implementation
Reset for next question:
Reset button is pressed for next question
No team is activated hence the output lights for 4 teams are off
Time counter is again ready to count time for this newround

## Slide 25
For ending the game winner declaration button is pressed
In this situation scores for 4 respective is T1(1),T2(0),T3(0),T4(2)
So the winner is Team 4
Team number is shown in DOT MATRIX display
Winner's score is shown in 7 segment display
Hardware Implementation
Winner Declaration:

## Slide 26
For restarting a new game we need to press the Master Reset Button
This will clear all the previous data that was recorded
Hardware Implementation
Preparing the system for a new game:

## Slide 27
Different Segment of Main Code
Variable declaration and initialization:

## Slide 28
Different Segment of Main Code
Buzzer lock ,Score update, Score store:

## Slide 29
Different Segment of Main Code
Buzzer lock ,Score update, Score store:

## Slide 30
Different Segment of Main Code
7 Segment Display:

## Slide 31
Different Segment of Main Code
DOT MATRIX Display:

## Slide 32
Different Segment of Main Code
Pin Planner:

## Slide 33: Work Progress
Understanding the Problem
Coding for different part of the problem
Combine all the coding in single file and compile
Update the code for uploading in a CPLD board
Full implementation in CPLD board
Observe the Vector Wave Form

## Slide 34: Individual Contribution
Name of the Task | Student ID
Designing the whole system | 2006066,2006077,2006091,2006096
Coding for priority encoder | 2006091
Coding for Counter | 2006091
Coding Score update and winner declaration | 2006096
Coding for 7 Segment Display | 2006066
Coding for DOT MATRIX Display | 2006077
Compiling Full code | 2006091,2006077
Debugging | 2006066,2006096
Upload in CPLD | 2006066,2006077,2006091,2006096

## Slide 35
Demonstration

## Slide 36
Thank you